## Slide 1: Binary to Hexa
Step 1: Write down the binary number and group the digits (0’s and 1’s) in sets of four. Start doing this from the right. If the leftmost group doesn’t have enough digits to make up a set of four, add extra 0’s to make a group.
Step 2: Write 8, 4, 2 and 1 below each group. These are the weights of the positions or place holders in the number (23, 22, 21 and 20).
Step 3: Every group of four in binary will give you one digit in hexadecimal. Multiply the 8, 4, 2 and 1’s by the digit above.
Step 4: Add the products within each set of four. Write the sums below the groups they belong to.
Step 5: The digits you get from the sums in each group will give you the hexadecimal number, from left to right.

## Slide 2: Binary to Hexa
Step 1 | 1010 | 1101
Step 2 | 8 4 2 1 | 8 4 2 1
Step 3 | 8 0 2 0 | 8 4 0 1
Step 4 | 10 (10 = 8+2) | 13 (13 = 8+4+1)
 | A | D
Step 5 | (10101101)2 = (AD)16 | 

## Slide 3: Hexa to binary
Step 1: Write down the hex number. If there are any, change the hex values represented by letters to their decimal equivalents.
Step 2: Each hex digit represents four binary digits and therefore is equal to a power of 2. The rightmost digit equals to 20 (1), the next one equals to 21 (2), the next one equals to 22 (4) and the leftmost one equals to 23 (8). Write these numbers (8, 4, 2 and 1) below the hex values.
Step 3: Determine which powers of two (8, 4, 2 or 1) sum up to your hex digits. For example, if one of your hex values is 10, this means 8 and 2 sum up to 10 (4 and 1 are not used). If your hex number is 2, only 2 is used; 8, 4 and 1 are not.
Step 4: Write down 1 below those 8, 4, 2 and 1’s that are used. Write down 0 below those that are not used.
Step 5: Read the 1’s and 0’s from left to right to get the binary equivalent of the given hex number.

## Slide 4: Hexa to binary
(4FA)16 = (?)2
 | 4 | F | A
Step 1 | 4 | 15 | 10
Step 2 | 8 4 2 1 | 8 4 2 1 | 8 4 2 1
Step 3 | 8 4 2 1 | 8 4 2 1 | 8 4 2 1
 | (4 = 4) | (15 = 8+4+2+1) | (10 = 8+2)
Step 4 | 0100 | 1111 | 1010
Step 5 | (4FA)16 = (10011111010)2 |  |