## Slide 1: PHYSICAL DIAGNOSITC
Memory
CAN message
DID range check
PID Test
CPID Test
DPID Test
DAC SI to Bus Message
How to read DIAG spec
Jul-16-2019
Ngoc Dao

## Slide 2: Memory (1/4)
  I. DID (Data Identifier)
    TCP / VCP setting data
    Timer, Counter, Function enable / disable ETC
    Compare value, range(Read & Write) with ALDL Spec
    Default Value Check target memory

## Slide 3: Memory (2/4)
  II. PID (Parameter Identifier)
    Stored vehicle state from vehicle message
    Battery state, Fuel info, Tire state......

## Slide 4: Memory (3/4)
  III. DPID (Data Packet Identifier)
    Trouble info
    Network status

## Slide 5: Memory (4/4)
  VI. CPID (Control Packet Identifier)
    Memory for Device Control
    Key pad, Call end, ECU reset, Disable Output…

## Slide 6: CAN message (1/8)
  CAN message includes: CAN ID (11 bits/29 bits) + Data
    Hecxa number
    Length: max 08 bytes
    Channel: HS/LS
    Send One or Periodic

## Slide 7: CAN message (2/8)
  II. CAN message types (1)
    Signal message
      Include information of vehicle state or events
      Signal message data is stored in PID memory
      No response message
      Structure:
  - Example:

## Slide 8: CAN message (3/8)
  III. CAN message types (2)
    2. Service message
      Message for Diagnostic Services
      Request and Response message is always in paired
      Structure:
  - Example:
Notes: $2xx = physical request CAN Identifier
$5xx = UUDT response CAN Identifier
$6xx = USDT response CAN Identifier

## Slide 9: CAN message (4/8)
  IV. Single Frame
  Example
Notes:     Valid Length : Defines a valid length in the frame
    Service ID : Service ID for request
    Sub Function : Sub Function ID – optional
    Required data : Data service detail

## Slide 10
CAN message (5/8)
  V. Multiple Frame
  Example
Notes:     Flow Status : Status information on the receiving side
    Block Size : Number of frames to receive after flow control
    ST min : Interval of frames to receive after flow control
    Sequence Number : Response frame number
    PCI: Protocol Control Information

## Slide 11
CAN message (6/8)
  VI. Protocol Control Information (PCI) formats for GMLAN

## Slide 12
CAN message (7/8)
  VII. General USDT Request/Response Sequence Examples

## Slide 13
CAN message (8/8)
  VIII. General UUDT Request/Response Sequence Examples

## Slide 14: DID Range Check (1/2)
Need to check:
  DID A0 (MEC) = $00 or not (use ATT tool)
    If A0=$00 > need to re-flashing TCP
  DID is ReadWrite/Write or Read only (Refer ALDL spec)
    If DID is read only then write >> Response: 03 7F 3B 31
  Restriction: Refer CG379
    Security Unlock
    Speed limitation
    Engine condition

## Slide 15: DID Range Check (2/2)
    To test:
      Send 24D 01 3E (to maintain Diagnostic service)
      Send 24D 02 27 01 (to unlock security)
      Send Speed < 3kph
        If speed >= 3kph: Response: 03 7F 3B 22
      Send Engine state = OFF
        If Engine = Running: Response: 03 7F 3B 22
      Send 24D 03 1A xx (xx is available DID) to read DID’s value
      Calculate Valid data range based on ALDL spec
      Send message to Write DID

## Slide 16: PID Test (1/2)
Vehicle Information is stored in PID memory. So to check PID value, we need to simulate signal which change PID’s data
Check ALDL spec to specify which CAN signal need to send
PID C03D:
Set Maximum of Rolling count: DID$67: byte3.4
Rolling Count signal: $3F9 00 xx xx 00 00 00 00 00 (HS, Oneshot)
Counter and Rolling Count Reset: $3F9 80 00 00 00 00 00 00 00 00 (HS, Oneshot)
To save to PID we need send two signals of Rolling Count, we call are Old and New
Case1: Old < new and new – old < 2000: Data will not be saved to PID until IGN OFF + Door Open
Case2: Old <new and new – old > = 2000: PID = Original + (new – old)/200
Case3: Old > new: PID = Original + ((FFFF – old) + new)/200
Note: the remainder will be saved to memory and will be added to next calculation

## Slide 17: PID Test (2/2)
C03D data is not changed when one of these conditions as below
  Engine OFF
  Send one signal
  Send two same signals
  Send 2 different signals but its delta < 2000 and mode is not DRx
  Example: C03D=$3E (Original)
    Send 00 00 then 00 50 > C03D=?
    Send 40 50 > C03D=?
    Send 80 00 > C03D=?
    Send 12 00 > C03D=?

## Slide 18: CPID Test (1/1)
CPID is Write only DID (Cannot read its values)
  CPID $00: Cancel All Active Device Control
  CPID $01: TCP I/O Controls
    Terminated normal call (Cannot terminate Collision, OCC initiated or Emergency call)
    3BA press
    Control Telltale status
  CPID $FD: System Basic Functions
    Disable all system output ($FD $80): All messages from the VCP/TCP ($97) will freeze for 5s or if cannot stop, it must be maintain data.
    Example: NCA message has no data, so it may be still running
    ECU reset (VCP/TCP soft reset) ($FD $40)
    Reset Source ID: Clear DTC from source ID (during this time VCP/TCP will not check DTC U-code – 5s impact)
    If environment is not in Restrictions, it shall send a negative response ($7F $E3 $XX $XX – Device Control Limits Exceeded)
    Bug: TCPXI-34178

## Slide 19: DPID Test (1/3)
Need to know how to setup some DTC – refer to
1. DPID $11: Communication, Memory, & General Software Errors
Check Current Status and History of Communication Errors (Loss of communication with GPS/NAD), Memory Errors (RAM Test Failed, Flash check sum..), General Software Errors (GPS reset, NAD reset…)…
2. DPID $12: Audio, BUB, & Keypad
Check Audio, BUB, & Keypad and Watch dog Time Stamp status
Ignition OFF/ON will reset all bit of DPID$12
Bug: TCPXI-34942
3. DPID $14, $15: GPS Latitude/Longtitude & PDOP

## Slide 20: DPID Test (2/3)
4. DPID $16: General Cellular/Calling
    Check Check signal strength, Call Mode and Free Band control, current PLMN (MCC & MNC), Call status Indicator
Notes: PLMN (Public Land Mobile Network):

## Slide 21: DPID Test (3/3)
6. DPID $17: Bluetooth
Check DTC B101D-37: Reset Case Type: MDM reset by MDM SW Watchdog/CPU Watchdog/MICOM external, MICOM reset by MICOM HW WatchdogWatchdog
Check Communicaton Errors 2, BUB/Audio Errors (Current Status/History)
Notes: PLMN (Public Land Mobile Network):

## Slide 22: DAC SI (1/2)
DACs Supported for GM Vehicles Table

## Slide 23: DAC SI (2/2)
DAC SI to Bus Message Table

## Slide 24: How to read Diagnostic spec (1/2)
    Request Message Definition

## Slide 25: How to read Diagnostic spec (2/2)
    Positive Response Message Definition
    Supported Negative Response Codes (RC_)

## Slide 26: References
GMW3110_V1.5
GIS-745 Abstract Diagnostic Access Revision 1.1 MY20 (Feb 2nd) – LGE
GEN11 GA TCP ALDL_MY21_v4.x Production-4-17-2019
CG379A
DIAG_vi2.nguyen_khanhly.nguyen
PD-TCExecution/vi2.nguyen